## Slide 1: Multimedia Data Speech and Audio
Dr Mike Spann
http://www.eee.bham.ac.uk/spannm
M.Spann@bham.ac.uk
Electronic, Electrical and Computer Engineering
Notes: <number>

## Slide 2: Content
Speech and sound signals
  Speech production
  Sampling speech signals
  What signals look and sound like?
    Time/Frequency components
  SFS demo
  Compression methods
Audio coding
  MP3 (perceptual coding)
Notes: <number>

## Slide 3: Speech Production
Notes: <number>

## Slide 4: Sampling and Quantizing A 5ms Speech Signal at 8kHz
Notes: <number>

## Slide 5: Sound Facts
The human ear hears sounds up to 20kHz
Nyquist theorem states that we have to sample at at least twice the highest frequency - hence we need to sample at 40kHz or better
8kHz sampling used for telephone speech, 44.1kHz used by CD audio, and, Digital Audio Tape (DAT) samples at 44kHz using 16-bit samples
Demo
  44kHz
  22kHz
  16kHz
  8kHz
  4kHz
  16bit
  8bit
Notes: <number>

## Slide 6: Examples of Speech Sounds
Examples of speech sounds are plosive, voiced and fricative.
Plosive
  A speech sound generated by a sudden release of air in the vocal tract. Plosive sounds can also not be maintained. Once you release the air the sound has ended.
Voiced
  A speech sound generated with vibrating vocal chords. Unvoiced speech sound is generated without the vibration of vocal chords.
Fricative
  A speech sound generated by turbulent air flow produced by a constriction. E.g., “shy”, “high”, “zoo” “thy”. They can be voiced or unvoiced.
Examples: [p] in pale, [ee] in seem, and, [f] in face
Words can contain mixtures .... e.g. “sap” or “puff”
Notes: <number>

## Slide 7: Speech Signals (SFS)
SFS demo (available on the course web page)
  Speech filing system (SFS) from Mark Huckvale at UCL.
  http://www.phon.ucl.ac.uk/resource/sfs/download.htm
  (demo.sfs - “BOX...AGO...BOX...AGO)
Time variation of signal amplitude
Spectrogram
Notes: <number>

## Slide 8: Spectrograms
A 2D plot showing the time/frequency distribution of a signal
Its essentially a ‘windowed’ frequency analysis
  The window ‘slides’ along the time axis
Very common in speech analysis
The spectrogram of a sinusoid is a horizontal line
More interestingly the spectrogram of an FM signal is a sinusoid!
FM signal
Violin
http://en.wikipedia.org/wiki/Spectrogram

## Slide 9: SFS Demonstration
The demonstration will show that spoken words can contain silences.
It will provide spectrograph examples which shows the frequencies present in the speech signal.
We will see how much of the intelligibility is in the high frequency components.
The low-pass filter example will provide a very simple simulation of sound after passing through a wall.
The sample waveform
The spectograph
(the frequency map of the signal above)
Notes: <number>

## Slide 10: Compressing Speech
Waveform Coding
Attempts to reproduce the original waveform.
64kbits/s -16kbits/s
Vocoding
A synthesised version of the signal.
1.2kbits/s-2.4kbits/s
(and as low as 300-600bps)
Hybrid Coding
Attempts to fill the gap between waveform and vocoding. Uses a combination of analysis and error minimisation.
4.8kbits/s - 9.6kbits/s
http://www-mobile.ecs.soton.ac.uk/speech_codecs/common_classes.html
Notes: <number>

## Slide 11: Compressing Speech
There is a good (but rather advanced) summary of speech compression using hybrid coders at http://www.data-compression.com/speech.html
Also includes a demo.

## Slide 12: Audio Coding (MP3)
‘MP3’ has almost become synonymous with the name of a player but its actually a standard for audio compression
  MP3 is actually MPEG-1 Layer-III
The German company Fraunhofer-Gesellshaft developed MP3 technology and now licenses the patent rights to the audio compression technology - United States Patent 5,579,430 for a "digital encoding process".
The inventors named on the MP3 patent are Bernhard Grill, Karl-Heinz Brandenburg, Thomas Sporer, Bernd Kurten, and Ernst Eberlein.

## Slide 13: Audio Coding (MP3)
The MPEG committee chose to recommend 3 audio compression methods of increasing complexity and demands on processing power.
Able to maintain excellent sound quality at very small file sizes.
The compression reduces an audio file to one-tenth of its original size.
  E.g. 40MB file  3.5MB
MP3 is actually MPEG-1 Layer-III
  They are 3 layers referred to as Audio Layer I, II and III
      Layer I is the simplest, a sub-band coder with a psychoacoustic mode
      Layer II adds more advanced bit allocation techniques and greater accuracy. This is used for digital radio (DAB, Digital Audio Broadcast)
      Layer III (MP3) adds a hybrid filterbank and non- uniform quantization plus advanced features like Huffman coding, 18 times higher frequency resolution and bit reservoir technique
Notes: <number>

## Slide 14: Audio Coding (MP3)
The standards require downward compatibility so, for example, a valid Layer III decoder must be able to decode any Layer I, II or III MPEG Audio stream. Similarly a layer II decoder should be able to decode Layer I and Layer II streams.
MPEG audio uses psychoacoustic models (perceptual coding), i.e., models of the way the human brain perceives sound.
  Music consists of many different components - not all of which are audible in the same way. For example, a soft flute may be hidden from the ear of the listener if a trumpet is played at the same time. The flute is still present, of course, but the listener is simply unable to perceive it: The flute is masked by the trumpet
  An mp3 implementation sees the trumpet represented with great precision and the flute more vaguely. This flexible method of representation helps to reduce the amount of information to be transmitted or stored - helping to minimize overall file size
Notes: <number>

## Slide 15: Simple Masking Example (from http://www.digitalradiotech.co.uk)
The figure shows the threshold of hearing curve and a single tone (sinewave) with a frequency of 1kHz.
The red curve (A) is the normal hearing threshold
The green curve (B) is the masking curve due to the tone (C) and the band of noise in yellow (D) at 1.5kHz cannot be perceived by the human ear because of the masking effect of the tone at 1kHz.
Notes: <number>

## Slide 16: Audio Coding (MP3)… continued
Including a psychoacoustical model means that masked tones can be removed from the bitstream to improve compression performance.
The coder calculates masking effects by an iterative process until it runs out of time.
File sizes
  As we would expect, quality descriptors are difficult to match to file sizes or compression ratios. For example, different users, different applications, different codecs will all have different expectations, requirements or different results.
  But as a very rough guide ...
    higher quality bit rates would be from 224 - 320kbps (closer to CD-quality).
    lower quality bit rates from 96kbps and below.
    Uncompressed audio as stored on an audio-CD has a bit rate of 1,411.2 kbit/s
Notes: <number>

## Slide 17: Audio Coding (MP3) demo
LAME is a high quality MP3 encoder/decoder
  http://lame.sourceforge.net/
RazorLame is a user friendly GUI for LAME allowing MP3 demonstrations
  http://www.dors.de/razorlame/index.php
We can create mp3 files at different compression ratios
Notes: <number>

## Slide 18: Summary
Speech and sound signals
  Speech production
  Sampling and quantisation
  What signals look and sound like (SFS demo) - spectrogram
  Compression approaches
Audio coding
  MP3 (perceptual coding)
  MP3 demonstrations
Notes: <number>

## Slide 19
This concludes our introduction to speech and audio.
You can find course information, including slides and supporting resources, on-line on the course web page at
Thank
You
http://www.eee.bham.ac.uk/spannm/Courses/ee1f2.htm
Notes: <number>