## Slide 1: Chapter 2 Multimedia Information Representation
2.1 Introduction
2.2 Digitization Principles
2.3 Text
2.4 Images
2.5 Audio
2.6 Video
Contents

## Slide 2: 2.1 Introduction
Codeword: a fixed number of bits representing a set of symbols, e.g) ASCII Code, FAX Run-length Code, … .
Signal Encoder
Signal Decoder
CODEC performs the conversion using some codewords
Network
Host
Host
Signal (or Data)
Data (or Signal)
Data (or Signal)
conversion
conversion
Audio-Video CODEC (Coder-Decoder)
conversion
conversion
Data
Data

## Slide 3: 2.2 Digitization Principles (1) (Analog  Digital)
Transfer
conversion
Encoder
Decoder
conversion
Networks
Bandlimiting
Filter
Sampler
Quantizer
& Coder
Analog
Digital
Decoder
Lowpass
Filter
Digital
A/D Converter
Analog
Host
Host
D/A Converter
- Spectrum VS. Bandwidth
- Signal bandwidth VS. Channel (Bandlimiting) bandwidth
- Cutoff frequency = min {Signal bandwidth, Bandlimiting bandwidth}
terms

## Slide 4
Bandlimiting
filter
Sampler
(sample-and-hold)
Quantizer
DAC
Lowpass
filter
Encoder
Decoder
A
B
D
E
G
H
Analog input signal
Analog output signal
대역 제한 필터
표본화
양자화
저 대역필터
DA 변환
Encoder
Network
부호화
C
F
clock
A
B
C
D
E
F
G
H
0
4
7
3
-4
-5
-3
5
0 000
0 100
0 111
0 011
1 100
1 101
1 011
0 101
time
PCM procedure
0 101(1-bit sign & 3-bit amplitude magnitude)

## Slide 5: 2.2 Digitization Principles(2) (Analog  Digital)
Analog Signal
  Bandwidth, B Hz, via bandlimiting channel (see the next slide)
Encoder
  Bandlimiting filter
  Sampling: 2B sps(samples per sec)  aliasing may happen !
  Quantizing: Aliasing filter for eliminating alias signals
    quantization interval q = 2(Vmax/2n)
    quantization error/noise = q/2
Decoder
  low-pass filter (= bandlimiting filter = anti-aliasing filter)
n: # of bits
Vmax: max(min) positive
(negative) signal
amplitude
Dynamic range of signal D D=20 log10(Vmax/Vmin)

## Slide 6: 2.2 Digitization Principles (3) (Analog  Digital)
Aliasing signal & its elimination
When does aliasing occur ?
If the sampling rate is lower than the Nyquist rate
time
amplitude
6KHz real signal
2KHz alias signal because of T’ = 3T
8Ksps
6KHz sine-wave is sampled at 8Ksps, lower than the Nyquist rate 12Ksps(26KHz)
Conclusion
All frequency components in the source signal that are higher in
frequency than half the sampling frequency being used will generate
related lower-frequency alias signal which will simply add to those
making up the original thereby causing it to become distorted
T
T’ = 3T
Resolution
Using “bandlimiting filter”, let’s pass only those Frequency
components up to that determined by the Nyquist rate
  bandlimiting filter = anti-aliasing filter = low-pass filter = reconstruction filter

## Slide 7: 2.2 Digitization Principles (4) (Analog  Digital)
Example 2.2
  An analog signal has a dynamic range of 40 dB. Find the magnitude of the quantization noise relative to the minimum signal amplitude if the quantizer uses 1) 6 bits and 2) 10 bits
Solution
   It follows that 40 = 20 log10(Vmax/Vmin) by assumption and finally the equation 102 = Vmax/Vmin results in Vmin = Vmax/100
   And the quantization noise is determined by  q/2 where, q is the quantization interval given by q =2(Vmax/2n). Thus  q/2= Vmax/2n.
   For n =6, q/2= Vmax/2n(= Vmax/64) > Vmin(=Vmax/100)  unacceptable !
  For n =10, q/2= Vmax/2n(= Vmax/1024) < Vmin(=Vmax/100)  acceptable !

## Slide 8
dB (decibel) : The decibel measures the relative strength of two signals or a signal at two different points p1 and p2
given by dB = 10 log10(p2/p1)
dB decibel
p1
p2
If a signal power is reduced to half at p2
such that p2=p1/2
10 log10(p2/p1) = 10 log10(0.5p1/p1)=
10 log10(1/2) = 10 log101- 10 log102= -3dB
irritating

## Slide 9: 2.3 Text
Unformatted Text, Plaintext
  String of fixed-size characters
  ASCII, Mosaic Characters, … .
Formatted Text
  String of characters of different sizes, styles &
  shapes with table, figures (graphics) & images
  Latex, Acrobat, … .
Hypertext
  Integrated set of documents comprising
  formatted & unformatted texts with linkages
  among them
  HTML, Postscripts, SGML, … .
Well-defined code-words
are used for Text Creation
& Manipulation

## Slide 10: 2.4 Images
Image (still picture) Classification
  Computer-generated images (computer graphics)
  e.g) palette files
  Digitized images of documents and/or pictures
    e.g) fax-scanned files, scanned color-image files
Graphics
  high-level language form: description of attributes of objects
  bit-map form: actual pixel-images
    gif: graphical interchange format
    tiff: tagged image file format
    srgp: simple raster graphics package
Digitized Documents
  Facsimile (FAX) machine, about 2Mbits/page(black-white/pixel)
    Pixel resolution: 8 per mm
    Line resolution: 3.85 or 7.7 per mm(100 or 200 lines per inch)
pixel (or pel):
picture element
VGA 640  480
(=열수  행수)
pixels
8-bits/pixel

## Slide 11: Digitized Pictures(1)
m-bit per pixel (pixel depth m)
  good-quality black-white picture: 8-bit/pixel(256 gray levels)
  colored-picture: 24-bit/pixel(R/G/B each 8-bit yielding 16 M colors)
Coloring Principles : How is color produced and represented ?
  Color gamut(색상범위 색대역): a whole spectrum of colors
  Three primary colors(삼원색): R (Red), G (Green), B (Blue)
    all kind colors are produced by using different proportions of these primary colors
    Additive Color Mixing (가산혼합) on a black surface
    Subtractive Color Mixing (감산혼합) on a white surface
Raster-Scan Principles: TV Screen or Computer CRT Monitor
  NTSC (National Television Standards Committee)-USA
    525(active 480) lines/frame & 60-time refresh rate/sec
  PAL (Phase Alternation Line)/CCIR/SECAM
    625(active 576) lines/frame & 50-time refresh/sec
pixel depth:
# of bits per pixel
참고 하기1
참고 하기2

## Slide 12: Digitized Pictures(2)
Scanning Order
1. N=525(NTSC) & 625(PAL/SECAM/CCIR)
2. fresh rate (Hz) = 60(NTSC) & 50(PAL/SECAM/CCIR)
3. M is determined by the aspect ratio (see the next slides)
1
2
3
4
5
N
1
2
3
M
frame : a complete set of N horizontal scan lines
TV
Scanning Method
Progressive scanning : 123…N: one frame
(전진주사)
Interlaced scanning : 135…N-1: first half frame (field)
(격월주사) 246…N: 2nd half frame (filed)
60 or 50 Hz refresh rate
30 or 25 Hz refresh rate
frame refresh rate: # of frames per sec
at least 50 Hz to avoid flickering
Retrace
Sweep
M x N 행렬

## Slide 13: Digitized Pictures(3)
Raster-Scan Principles
  Raster(래스터): a finely-focused electro beam
  Phosphor(발광체): a light-sensitive material that emits light when energized
    white-sensitive phosphor: a single electron beam used
    color-sensitive phosphor : each pixel comprises a set of three color-sensitive phosphors, one each for R, G, B signals, called phosphor triad
    beam signal may be either analog or digital form
Pixel Depth: # of bits per pixel
  CLUT (Color Look-Up Table): 24-bit/pixel yields 224 colors. But eye discriminates between some ranges of colors hence, each pixel value is used as an index on CLTT of 256 colors (compression achieved !)
spot size: 0.635mm(0.025inch)
#FFFFFF
in HTML

## Slide 14: Digitized Pictures(4)
Aspect Ratio: ratio of the screen width to the screen height
  NTSC, 525 scan lines/frame ⇒ 480(45) data (control) lines
    4/3 aspect ratio ⇒ 480  4/3(=640) pixels/line
    16/9 aspect ratio ⇒ 480  16/9(=853.33) pixels/line
  PAL/CCIR/SECAM 625 lines/frame ⇒ 576(49) data (control) lines
    4/3 aspect ratio ⇒ 576  4/3(=768) pixels/line
    16/9 aspect ratio ⇒ 576  16/9(=1024) pixels/line
Computer Graphics Array
standard
resolution
#of colors
Bytes/frame
VGA
640 x 480 x 8
256
307.2K
XGA
640 x 480 x 16
1024 x 768 x 8
64K
256
614.4K
786.432K
SVGA
800 x 600 x 16
1024 x 768 x 8
1024 x 768 x 24
64K
256
16M
960K
786.432K
2359.296K
refresh rate:
50-70Hz
Representing an MN pixels under a particular aspect ratio

## Slide 15: Digitized Pictures
DVI (Digital Visual Interface)
기존 그래픽 카드에는 램댁(RAMDAC)이 들어있어 디지털 신호를 아날로그 신호로 바꾸어 화면을 표시함.
기존 CRT모니터가 아날로그 방식이기 때문임.
그러나 LCD는 완전 디지털이기 때문에 굳이 아날로그로 변경할 이유가 없기 때문에 DVI단자를 만들어 디지털로 바로 전송하게 하는 것임.

## Slide 16: Digitized Pictures(5)
Example 2.3
Derive the time to transmit the following digitized images at both 64Kbps and 1.5Mbps networks
  a 6404808 VGA-compatible image
  a 102476824 SVGA-compatible image
Solution
The size of each image in bit is as follows
  a VGA image = 6404808 = 2.46Mbits
  an SVGA image = 102476824 =18.88Mbits
The time to transmit each image is given as follows
  at 64Kbps : VGA = 2.46Mbits/64Kbps = [2.46106]/[64 103] = 38.4 sec. SVGA = [18.88106]/[64 103] = 295 sec.
  at 1.5Mbps: VGA = 2.46Mbits/1.5Mbps = [2.46106]/[1.5 106] = 1.64 sec. SVGA = [18.88106]/[1.5 106] = 12.59 sec.

## Slide 17: Digitized Pictures(6)
Digital Cameras & Scanners
  (Still image cameras) 2-D grid of photo-sites (빛 감지 diode), light-sensitive cells, made of charge-coupled devices (CCD’s)
    level of light intensity on each photosites is converted into a digital value using an AD converter when the shutter is activated
  (Scanners) single-row of photo-sites is exposed in time- sequence with the scanning operation
  How are color images obtained ?
    each photosite/pixel is coated with R/B/G filter & the color is determined by the level of it together with 8 neighbors in a 3 x 3 grid structure
    use of three separate exposures of a single photosite, say, first R filter, 2nd G filter, and finally B filter
    use of three separate image sensors per pixel
  e.g) TIFF (tagged image file format), TIFF/EP for electronic photography
General consumer
Photo studio
professional

## Slide 18: 2.5 Audio
Typical Audio Types
  Speech signal for interpersonal application such as (video) telephony
  Music-quality audio such as CD-on-demand & broadcast TV
    synthesizer
    microphone
    loudspeaker
Human speech: 50Hz -10KHz (4Khz in a plain-old-telephone system)
- 2 x 10K or 2 x 8K sps  monaural (mono) speech
- (2 x 10K) x 2 or (2 x 8K) x 2 sps  stereophonic speech
- ideally, 12 bits/sample
2. Human audible music: 15Hz - 20KHz
- 2 x 20K sps  monaural (mono) music
- (2 x 20K) x 2 sps  stereophonic music
- ideally, 16 bits/sample
Basics on Audio Signals
sps: samples per sec.

## Slide 19: PCM Speech(1)
Human Voice over PSTN
  200Hz-3.4Khz bandlimiting channel: about less than 4Khz
  8K(2x4K) sps, 8bits/sample : ITU-T G.711(PCM) recommendation
  Companding (compressing/expanding)
    1-bit: polarity, 3-bit: segment code, 4-bit: quantization code
Compander
(compressor/expander)
Pure
PCM signals
Enhanced
PCM signals
Because the human ears are more sensitive to noise on quiet signals than it is on loud signals. Hence the effect of quantization noise (error) can be reduced with companding
Why companding ?
Equal (linear) interval quantization & same level of quantization error
Non-linear (unequal) interval quantization & narrower intervals for smaller amplitude signals
Irrespective of the magnitude of the input signal , the same error level for both low (quiet) signals and high (loud) signals is produced

## Slide 20: PCM Speech(2)
Companding Example: 5-bit per sample(1-bit polarity, 2-bit segment code, & 2-bit quantization code)
11 10 01 00
11 10 01 00
11 10 01 00
11 10 01 00
Linear quantization intervals
01
00
10
11
Segment codes(+)
00 01 10 11
00 01 10 11
00 01 10 11
00 01 10 11
10
11
01
00
Segment codes(-)
Polarity: 1
Polarity: 0
+V
-V
Narrower intervals for smaller amplitude
signal
compressing
+V
-V

## Slide 21: PCM Speech(3)
Companding Example: 5-bit per sample(1-bit polarity, 2-bit segment code, & 2-bit quantization code)
11 10 01 00
11 10 01 00
11 10 01 00
11 10 01 00
Linear quantization intervals
01
00
10
11
Segment codes(+)
00 01 10 11
00 01 10 11
00 01 10 11
00 01 10 11
10
11
01
00
Segment codes(-)
Polarity: 1
Polarity: 0
+V
-V
Wider intervals for smaller amplitude
signal
Expanding

## Slide 22: PCM Speech(4)
Two Companding Codewords for PCM
  μ -law: North America & East Asia
  A-law: Europe
+127
+96
+64
+32
+0
-0
-32
-64
-96
-127
1 0000000
1 0011111
1 0111111
1 1011111
1 1111111
0 1111111
0 1011111
0 0111111
0 0011111
0 0000000
1 1111111
1 1100000
1 1000000
1 0100000
1 0000000
0 0000000
0 0100000
0 1000000
0 1100000
0 1111111
1’s complement
μ-law
A-law
Sign bit (polarity)
“Signed & magnitude” representation

## Slide 23: CD-Quality Audio
Human audible bandwidth: 15Hz-20Khz  40Ksps
In CD-ROMs, more higher, say, 44.1Ksps & 16-bit/sample used
  bit rate for channel = sampling rate x bits per sample
    = 44.1 x 103 x 16 = 705.6 Kbps
  total rate required for stereophonic music
      = 2 x 705.6 = 1.411 Mbps
  storage capacity for a 1 hour CD-ROM title
      = 1.411 x 60 x 60 = 634.95 Mbytes
  this takes (634.95 x 106 x 8)/(10 x 106) = 8.5 min. down-loading time via a 10Mbps link network !

## Slide 24: Synthesized Audio
A digitized audio requires a large amount of memory while a synthesized audio is 1) 2 or 3 orders of magnitude less 2) much easier to edit & to mix several passes together
An audio/sound synthesizer: computer + keyboard + a set of sound generators + interfaces for instruments (elec. guitar)
* MIDI (Music Instrument Digital Interface): Standard I/O interfaces
  Messages (status byte + data bytes)
  Connectors, Cables, & Electrical Signals

## Slide 25: 2.6 Video (Motion): Broadcast TV
  Entertainment: Broadcast TV, VCR/DVD Recordings
  Interpersonal: Video Telephony & Videoconferencing
  Interactive: Video Clips on PC Windows
Video Applications
Scanning Sequences: Interlaced Scanning
  To minimize the amount of tx bandwidth, a frame is divided into two halves called fields
    e.g) 525-line 50-time frame refresh rate/sec.
      - 262.5 odd lines 50-time field rate/sec.
      - 262.5 even lines 50-time field rate/sec.
  In reality,
  525-line 25-time frame refresh rate/sec.

## Slide 26: Broadcast TV(2)
Color Signals
  Three properties of a color
    - Brightness, Hue (Tint) & Saturation
  Color production: an equation of R, G, and B phosphors
    - 0.299 R + 0.587 G + 0.114 B where, 0.299+0.587+0.114=1
  Luminance refers to the brightness of a source, the hue & the saturation called, chrominance characteristics
    say, luminance Ys = 0.299 Rs + 0.587 Gs + 0.114 Bs
    Ys: magnitude of luminance signal
    Rs, Gs, Bs: magnitudes of three major colors
  Two color difference signals: Blue chrominance Cb and Red chrominance Cr
    - Cb = Bs-Ys, Cr = Rs -Ys
Luminance: 휘도
Brightness: 밝기
Hue (Tint): 색조/색상
Saturation: 채도
Chrominance: 색차

## Slide 27: Broadcast TV(3)
Chrominance Components
  Composite Video Signal for Transmission
    - Ys, Cb, and Cr signals are combined together and signal differences are scaled down before transmission
  In PAL
    - Y = 0.299 R + 0.587 G + 0.114 B
    U(Cb) = 0.493(B-Y) = -0.147R-0.289G+0.437B
    V(Cr ) = 0.877(R-Y) = 0.615R-0.515G-0.1B
  In NTSC
    - Y = 0.299 R + 0.587 G + 0.114 B
    I(Cb) = 0.74(R-Y)-0.27(B-Y) = 0.599R-0.276G-0.324B
    Q(Cr ) = 0.48(R-Y)+0.41(B-Y) = 0.212R-0.528+0.311B

## Slide 28: Digital Video
Advantages of DV
  Easy to store in computer
  Easy to edit and integrate with other types
  Easy to digitize three RGB component signals
The resolution of eyes are less sensitive for color than it is for luminance. Hence, two chrominance signals can tolerate a reduced resolution
  Transmission bandwidth is achieved by using the luminance and two color difference signals, instead of the RGB signals directly.
  CCIR-601 Recommendations: standard for the digitization of video pictures

## Slide 29: Digital Video(2)
4:2:2 format(CCIR-601)
  Recommendation for use in TV studio
  Three component (analog) video signals may have bandwidths
    up to 6Mhz for the luminance ⇒ 12Mhz sps
    less than 3Mhz for the two chrominance signals ⇒ 6 Mhz sps
    In reality, 13.5M sps for luminance, 6.75 M sps for the two chrominance signals
  In NTSC(525-line) system, total line sweep time 63.56μsec =
  retrace time 11.56 μsec + an active line sweep time 52 μsec
  In PAL(625-line) system, total line sweep time 64μsec =
    retrace time 12 μsec + an active line sweep time 52 μsec
Line sampling rate:
5210-613.5106 = 702 samples/line
In reality, 720 samples/line
Line sampling rate:
5210-66.75106 = 351 samples/line
In reality, 360 samples/line
4Y samples for every 2Cb and 2Cr samples(4:2:2)
Orthogonal sampling
Y
Cb
Cr

## Slide 30: Digital Video(3)
4:2:2 Format Bit Rate & Storage (NTSC 525-line)
  The number of active (visible) lines: 480
  The number of samples per line: 720
Resolution of luminance Y = 720480
Two chrominance signals Cb = Cr = 360480
  Line sampling rate: 13.5sps for Y & 6.75sps for both Cb & Cr
  Bits per sample: 8 bits
Bit rate per line = 13.51068 + 2(6.751068) = 216Mbps
Bits per line = 7208 + 2(3608) = 11.52Kbits
Bits per frame = 48011.52 = 5.5296Mbits
Bits for 1.5 hrs Video assuming 60 refresh rate = 5.5296601.53600
= 223.9488GBytes
PAL 625-line
576
720
720576
360576
576
6.63555Mbits
6.6355550

## Slide 31: Digital Video(4)
4:2:0 Format
  used in Digital Broadcast Applications
  interlaced scanning with the absence of chrominance samples in alternative lines
  525-line system
    Y = 720480(the same as 4:2:2 format), Cb = Cr = 360240
  625-line system
    Y = 720576, Cb = Cr = 360288
  bit rate per line: 13.51068 + 2(3.3751068) = 162Mbps
HDTV Format
  used in High-Definition Television (four times bit rate)
  4/3 14401152 pixels(50/60 Hz refresh rate) & 16/9 wide-screen 19201152 pixels(25/30 Hz) with # of visible lines per frame 1080

## Slide 32: Digital Video(5)
SIF (Source Intermediate Format), 4:1:1 Format
  used in Video Cassette Recorders (VCRs)
  progressive (non-interlaced) scanning since it is intended for storage applications
  Half of 4:2:0 format: “Subsampling & Temporal Resolution”
  525-line system
    Y = 360240, Cb = Cr = 180120
  625-line system
    Y = 360288, Cb = Cr = 180144
  bit rate per line
    6.751068 + 2(1.68751068) = 81Mbps

## Slide 33: Digital Video(6)
CIF (Common Intermediate Format), 4:1:1 format
  used in Video Conferencing applications
  spatial resolution of the SIF 625-line system plus temporal resolution of the SIF 525-line system
    Y = 360288, Cb = Cr = 180144
    refresh rate: 30 Hz
    bit rate per line: 6.751068 + 2(1.68751068) = 81Mbps
  many variants for videoconferencing using desktop PCs or ISDN/PSTN
    say, typically 4 or 16 64Kbps channels used
      4CIF: Y = 720576, Cb = Cr = 360288
      16CIF: Y = 14401152, Cb = Cr = 720576

## Slide 34: Digital Video(7)
QCIF (Quarter CIF), 4:1:1 Format
  used in Video Telephony applications
  half spatial resolution of the CIF and either half or quarter temporal resolution of the CIF
    Y = 180144, Cb = Cr = 9072
    refresh rate: 15 or 7.5 Hz
    bit rate per line: 3.3751068 + 2(0.843751068) = 81Mbps
  a lower version is typically used for single 64Kbps channel ISDN or PSTN with modems: sub-QCIF(SQCIF)
      Y = 12896, Cb = Cr = 6448

## Slide 35: Digital Video(8)
PC Video Digitization
Digitization Format | System | Spatial Resolution | Temporal Resolution
4:2:2 | 525-line 625-line | Y = 640480, Cb = Cr = 320240 Y = 768576, Cb = Cr = 384288 | 60Hz 50Hz
SIF | 525-line 625-line | Y = 320240, Cb = Cr = 160240 Y = 384288, Cb = Cr = 192144 | 30Hz 25Hz
CIF |  | Y = 384288, Cb = Cr = 192144 | 30Hz
QCIF |  | Y = 192144, Cb = Cr = 9672 | 15/7.5Hz
- Video capture board or S/W required - All PC monitors use “progressive (non-interlaced) scanning” |  |  |