## Slide 1: Multimedia Data Video Compression The MPEG-1 Standard
Dr Sandra I. Woolley
http://www.eee.bham.ac.uk/woolleysi
S.I.Woolley@bham.ac.uk
Electronic, Electrical and Computer Engineering
This lecture provides a short introduction to video compression using the original MPEG-1 standard as an example.
These notes are based on original slides from Dr N. Flowers.
Notes: <number>

## Slide 2: Contents
Analogue TV
Basic digital TV – the problem
MPEG-1 definition
Decimation (spatial, temporal and colour)
Spatial compression
Temporal compression
Difference coding
Motion compensation
Notes: <number>

## Slide 3: Analogue Television
How much bandwidth would we need for uncompressed digital television?
The European analogue TV format was 625 scan lines, 25 interlaced frames per second, 4:3 aspect ratio
It used interlacing to reduce the vertical resolution to 312.5 lines
Horizontal resolution was 312.5*(4/3) = 417 lines
Bandwidth required = 625*417*25 = 6.5MHz
Analogue colour information was quite cleverly added without increasing bandwidth (NTSC, PAL and SECAM standards)
http://www.answers.com/topic/interlace?cat=technology
http://en.wikipedia.org/wiki/PAL
Notes: <number>

## Slide 4: Digital Television – Raw Video
For digital use, let’s say an 8 bit resolution is adequate.
For colour pictures we will need Red, Green and Blue (RGB.)
To digitise, we need to sample at twice the highest frequency* (6.5MHz) and convert three colours (RGB) at 8 bits each.
Bitrate = (6.5x2) x 3 x 8 = 312 Mbits/Sec
(compare with analogue bandwidth of 6.5MHz)
Digitising the analogue television signal created a huge digital bandwidth requirement. We needed some efficient compression.
*This is called Nyquist’s Theorem
Notes: <number>

## Slide 5: Coding of Moving Pictures and Associated Audio for Digital Storage Media at up to about 1.5 Mbits/sec. International Standard IS-11172, completed in 10.92
Moving Picture Experts Group – 1st phase
Video CD - A standard for video on CD’s at ‘VHS’ quality.
Audio CD’s have a data rate of 1.5Mb/s – video has a raw data rate of 312Mb/s – 200 times higher!
Something had to be lost.
Commonly known as MPEG-1
Notes: <number>

## Slide 6: MPEG-1 Decimation
This means just throwing data away ...
Where can we decimate?
  Spatial
  Colour
  Temporal
  (also audio)
Temporal - Interlacing is dropped giving 25 full frames per second
Notes: <number>

## Slide 7: Spatial Decimation
European broadcast TV standard
Resolution is reduced to 352 (width) by 288 (height) pixels
  Source Input Format (SIF)
352 pixels
288
pixels
417 lines
625
Half-lines
Notes: <number>

## Slide 8: Colour Decimation
Human perception is most sensitive to luminance (brightness) changes
Colour is less important e.g. a black and white photograph is still recognisable
RGB encoding is wasteful – human perception tolerates poorer colour.
Use YUV and only encode chrominance (UV) at half resolution in each direction (176 by 144) – Quarter SIF.) This gives 0.25 data for U and V compared to Y.
Notes: <number>

## Slide 9: Colour Decimation Example
Original (100%)
0.5 UV (25%)
0.25 UV (6.25%)
0.2 UV (4%)
0.1 UV (1%)
0.0 UV (0%)
Notes: <number>

## Slide 10: Temporal Decimation
Three standards for frame rate in use today
  Cinema uses 24 FPS
  European TV uses 25 FPS
  American TV uses 30 FPS
Lowest acceptable frame rate is 25 FPS so little decimation can be achieved for Video CD
MPEG-1 does allow much lower frame rates e.g. for internet video – but quality is reduced
Notes: <number>

## Slide 11: Decimation – The Result
After throwing away all this information, we still have a data rate of (assuming 8 bits per YUV):
  Y = (352*288) * 25 * 8 = 20.3 Mb/s
  U = (352/2 * 288/2) * 25 * 8 = 5.07 Mb/s
  V = (352/2 * 288/2) * 25 * 8 = 5.07 Mb/s
  TOTAL (for video) = 30.45 Mb/s
  MPEG 1 audio runs at 128Kb/s
  Video CD - Target is 1.5Mb/sec
  Space for video = 1.5 – 0.128Mb/s = 1.372Mb/s
So now use compression to get a saving of 22:1
Notes: <number>

## Slide 12: Spatial Compression
A video is a sequence of images – and images can be compressed.
JPEG uses lossy compression – typical compression ratios are around 10:1 and, with deteriorating, quality up toward 20:1
We could just compress images and send these.
Time does not enter into the process.
This is called intra-coding (intra = within)
Notes: <number>

## Slide 13: Spatial Compression
Very similar to JPEG
Image divided into 8 by 8 pixel sub-blocks
Number of blocks = 352/8 by 288/8 = 44 by 36 blocks
Each block DCT coded
Quantisation - dropping low-amplitude coefficients
Huffman coded
This produces a complete frame called an Intra frame (I)
Notes: <number>

## Slide 14: Temporal Compression
Spatial compression does not take into account similarities between adjacent frames
Talking Heads - Backgrounds don’t change
Consecutive images (1/25th second apart) are very similar
Just send the difference between adjacent frames
Notes: <number>

## Slide 15: Difference Coding
Only send difference between this frame and previous frame
Result is very sparse – high compression now possible using block-based DCT as before
Notes: <number>

## Slide 16: Difference Coding
Using the previous frame and the difference frame we can recreate the original – this is called a predicted frame (P)
This recreated frame can then be used to form the next frame and the process is repeated.
Notes: <number>

## Slide 17: Difference Coding
Difference coding is good for ‘talking heads’
Not good for scenes with lots of movement
Notes: <number>

## Slide 18: Motion Compensation
Difference coding is good, but often an object will simply change position between frames.
DCT coding not as good as for ‘sparse’ difference image.
Notes: <number>

## Slide 19: Motion Compensation
Video is three-dimensional (X,Y, Time)
DCT coding reduces information in X and Y
Stationary objects do not move in time
Motion compensation takes time into account
No need to code the image of the object – just send a motion vector indicating where it has moved to
Notes: <number>

## Slide 20: Motion Compensation
Called Motion Compensation since we actually adjust the position of the object to compensate for the movement
Notes: <number>

## Slide 21: Motion Compensation – The Problems
Objects rarely move and retain their shape.
If object moves and changes shape a little:
  Find movement and send motion vector.
  Subtract moved object in last frame from object in new frame.
  DCT code the difference.
But what is an object? We have an array of pixels.
Could try and segment image into separate objects – but very intense processing!
Simple option - split image up into blocks that don’t correspond to ‘objects’ in the image – macroblocks
Notes: <number>

## Slide 22: Macroblocks
Macroblocks can be any shape or size
  If small, then we need to send lots of vectors
  If large, then we are unlikely to find a matching macroblock
MPEG-1 uses a 16 by 16 pixel macroblock
Each macroblock is the unit for motion compensation
  Find macroblock in previous frame similar to this one
  If match found, send motion vector
  Subtract this macroblock from previous displaced macroblock
  DCT code the difference
If no matching block found, abandon motion compensation and just DCT code the macroblock
Notes: <number>

## Slide 23: MPEG-1 Compression
Eyes - difference data DCT coded
Ball - motion vector coded, actual image data not coded
Rabbit - Intra coded with no temporal compression
Coding method varies between macroblocks
Notes: <number>

## Slide 24: Group of Pictures - GOP
Problem with P frames is any errors are propagated (like making copies of copies of copies) - so we regularly send full (I) frames to eliminate errors
Every 0.5 seconds approx we send a full frame (I)
I P P P P P P P P P P P I P P P P P P P P P P P I P P
 GOP 
In the event of an error, data stream is resynchronised after 12/25th of a second (or 15/30th for USA)
The sequence between ‘I’s is called a Group Of Pictures
Notes: <number>

## Slide 25: Additional MPEG-1 complexities
Motion compensation allows significant data reduction….. but only takes into account time moving forward
Bidirectional frames (B) - predicted from past and future frames
Notes: <number>

## Slide 26: Summary
Analogue TV
Basic digital TV – the bandwidth problem
MPEG-1 definition
Decimation (spatial, temporal and colour)
Spatial compression
Temporal compression
Difference coding
Motion compensation
Notes: <number>

## Slide 27
This concludes our introduction to video compression.
You can find course information, including slides and supporting resources, on-line on the course web page at
Thank
You
http://www.eee.bham.ac.uk/woolleysi/teaching/multimedia.htm
Notes: <number>