## Slide 1: Multimedia Data Introduction to Lossless Data Compression
Dr Sandra I. Woolley
http://www.eee.bham.ac.uk/woolleysi
S.I.Woolley@bham.ac.uk
Electronic, Electrical and Computer Engineering
Notes: <number>

## Slide 2: Lossless Compression
An introduction to lossless compression methods including:-
  Run-length coding
  Huffman coding
  Lempel-Ziv
Notes: <number>

## Slide 3: Run-Length Coding (Reminder)
Run-length coding is a very simple example of lossless data compression. Consider the repeated pixels values in an image …
000000000000555500000000 compresses to (12,0)(4,5)(8,0)
24 bytes reduced to 6 gives a compression ratio of 24/6 = 4:1
As we noted earlier, there must be an agreement between sending compressor and receiving decompressor on the format of the compressed stream which could be (count, value) or (value, count).
We also noted that a source without runs of repeated symbols would expand using this method.
Notes: <number>

## Slide 4: Patent Issues
There is a long history of patent issues in the field of data compression. Even run length coding is patented.
From the comp.compression faq :
Tsukiyama has two patents on run length encoding: 4,586,027 and 4,872,009 granted in 1986 and 1989 respectively. The first one covers run length encoding in its most primitive form: a length byte followed by the repeated byte. The second patent covers the 'invention' of limiting the run length to 16 bytes and thus the encoding of the length on 4 bits.
Here is the start of claim 1 of patent 4,872,009, just for interest:
“A method of transforming an input data string comprising a plurality
of data bytes, said plurality including portions of a plurality of
consecutive data bytes identical to one another, wherein said data
bytes may be of a plurality of types, each type representing different
information, said method comprising the steps of: [...]”
Notes: <number>

## Slide 5: Huffman Compression
Source character frequency statistics are used to allocate codewords for output.
Compression can be achieved by allocating shorter codewords to the more frequently occurring characters. For example, in Morse code
E= • Y= - • - -).
Notes: <number>

## Slide 6: Huffman Compression
By arranging the source alphabet in descending order of probability, then repeatedly adding the two lowest probabilities and resorting, a Huffman tree can be generated.
The resultant codewords are formed by tracing the tree path from the root node to the codeword leaf.
Rewriting the table as a tree, 0s and 1s are assigned to the branches. The codewords for each symbols are simply constructed by following the path to their nodes.
Notes: <number>

## Slide 7: Huffman Compression
Notes: <number>

## Slide 8: Is That All There is to it?
David Huffman invented this method in 1951 while a graduate student of Robert Fano. He did not invent the idea of a coding tree. His insight was that by assigning the probabilities of the longest codes first and then proceeding along the branches of the tree toward the root, he could arrive at an optimal solution every time.
Fano and Shannon had tried to work the problem in the opposite direction, from the root to the leaves, a less efficient solution.
When presented with his student's discovery, Huffman recalls, Fano is said to have exclaimed: "Is that all there is to it!"
From the September 1991 issue of Scientific American, pp. 54, 58.
Top right – Original figures from IRE Proc. Sept 1952
Notes: <number>

## Slide 9: Huffman Compression
Questions:
What is meant by the ‘prefix property’ of Huffman?
What types of sources would Huffman compress well and what types would it compress inefficiently?
How would it perform on images or graphics?
Notes: <number>

## Slide 10: Static and Adaptive Compression
Compression algorithms remove source redundancy by using some definition (model) of the source characteristics.
Compression algorithms which use a pre-defined source model are static.
Algorithms which use the data itself to fully or partially define this model are referred to as adaptive.
Static implementations can achieve very good compression ratios for well defined sources.
Adaptive algorithms are more versatile, and update their source models according to current characteristics. However, they have lower compression performance, at least until a suitable model is properly generated.
Notes: <number>

## Slide 11: Lempel-Ziv Compression
Lempel-Ziv published mathematical journal papers in 1977 and 1978 on two compression algorithms (these are often abbreviated as LZ’77 and LZ’78)
Welch popularised them in1984
LZW was implemented in many popular compression methods including .GIF image compression.
It is lossless and universal (adaptive)
It exploits string-based redundancy
It is not good for image compression (why?)
Notes: <number>

## Slide 12: Lempel-Ziv Dictionaries
How they work :-
Parse data character by character generating a dictionary of previously seen strings
LZ’77 uses a sliding window dictionary
LZ’78 uses a full dictionary history
LZ’78 Description
With a source of 8-bits/character (i.e., source values of 0-255.) Extra characters will be needed to describe strings for in our dictionary. So we will need more than 8 bits.
Start with output using 9-bits. So now we can use values from 0-511.
We will need to reserve some characters for ‘special codewords’ say, 256-262, so dictionary entries would begin at 263.
We can refer to dictionary entries as D1, D2, D3 etc. (equivalent to 263, 264, 265 etc.)
Dictionaries typically grow to 12- and 15-bit lengths.
Notes: <number>

## Slide 13
Notes: <number>

## Slide 14: Lempel-Ziv … continued
So the compressed output is “THE<D1>RE<D3><D5>ES”.
Each of these 10 output codewords is represented using 9 bits.
So the compressed output uses 90 bits.
Calculating the compression ratio
The original source contains 13x8-bit characters (=104 bits) and the compressed output contains 10x9-bit codewords (=90 bits).
So the compression ratio = (old size/new size):1 = 1.156:1
So some compression was achieved. Despite the fact that this simple implementation of Lempel-Ziv would normally start by expanding the data, this example has achieved compression. This was because the compressed string was particularly high in repeating strings, which is exactly the type of redundancy the method exploits.
Notes: <number>

## Slide 15: Lempel-Ziv Exercises
How is decompression performed? Does the dictionary need to be sent?
Using the source output from our example, build a dictionary and decompress the source.
Compress the strings “rintintin” and “lesslosslesslossless” (using “” to represent the space character).
Decompress the string “WHERET<D2>Y<D2><D4><D6><D2>N” (“” represents the space character).
Now compress the string “WHERETHEYHERETHEN” (using “” to represent the space character).
Only for the very keen …. What is the “LZ exception”?
(an example can be found at http://www.dogma.net/markn/articles/lzw/lzw.htm)
Notes: <number>

## Slide 16
This concludes our introduction to selected lossless compression.
You can find course information, including slides and supporting resources, on-line on the course web page at
Thank
You
http://www.eee.bham.ac.uk/woolleysi/teaching/multimedia.htm
Notes: <number>