## Slide 1: Multimedia Data Speech and Audio
Dr Sandra I. Woolley
http://www.eee.bham.ac.uk/woolleysi
S.I.Woolley@bham.ac.uk
Electronic, Electrical and Computer Engineering
Notes: <number>

## Slide 2: Content
Speech and sound signals
  What signals look and sound like?
  (SFS demo)
  Frequency components
  Low and high-pass filtering
  Compression methods
Audio coding
  MP3 (perceptual coding)
Notes: <number>

## Slide 3: Speech Production
Notes: <number>

## Slide 4: Sampling and Quantizing A 5ms Speech Signal at 8kHz
Notes: <number>

## Slide 5: Sound Facts
The human ear hears sounds up to 20kHz.
Nyquist theorem states that we have to sample at at least twice the highest frequency - hence we need to sample at 40kHz or better.
8kHz sampling used for telephone speech, 44.1kHz used by CD audio, and, Digital Audio Tape (DAT) samples at 44kHz using 16-bit samples.
Notes: <number>

## Slide 6: Examples of Speech Sounds
Examples of speech sounds are plosive, voiced and fricative.
Plosive
  A speech sound generated by a sudden release of air in the vocal tract.
Voiced
  A speech sound generated with vibrating vocal chords. Unvoiced speech sound is generated without the vibration of vocal chords.
Fricative
  A speech sound generated by turbulent air flow produced by a constriction. E.g., “shy”, “high”, “zoo” “thy”. They can be voiced or unvoiced.
Examples: [p] in pale, [ee] in seem, and, [f] in face
Words can contain mixtures .... e.g. “sap” or “puff”
Notes: <number>

## Slide 7: SFS
Notes: <number>

## Slide 8: Speech Signals (SFS)
SFS demo (available on the course web page)
  Speech filing system (SFS) from Mark Huckvale at UCL.
  http://www.phon.ucl.ac.uk/resource/sfs/download.htm
  (demo.sfs - “BOX...AGO...BOX...AGO)
Notes: <number>

## Slide 9: SFS Demonstration
The demonstration will show that spoken words can contain silences.
It will provide spectrograph examples which shows the frequencies present in the speech signal.
We will see how much of the intelligibility is in the high frequency components.
The low-pass filter example will provide a very simple simulation of sound after passing through a wall.
The sample waveform
The spectograph
(the frequency map of the signal above)
Notes: <number>

## Slide 10: Compressing Speech
Waveform Coding
Attempts to reproduce the original waveform.
64kbits/s -16kbits/s
Vocoding
A synthesised version of the signal.
1.2kbits/s-2.4kbits/s
(and as low as 300-600bps)
Hybrid Coding
Attempts to fill the gap between waveform and vocoding. Uses a combination of analysis and error minimisation.
4.8kbits/s - 9.6kbits/s
http://www-mobile.ecs.soton.ac.uk/speech_codecs/common_classes.html
Notes: <number>

## Slide 11: Real Speech Example
This sample was taken from a movie recorded in 1962 at the cineradiographic facility of the Wenner-Gren Research Laboratory at Nortull's Hospital, Stockholm, Sweden.
On-line at Haskins Laboratories (http://www.haskins.yale.edu/Haskins/TIEDE/database.html)
Recognising speech is a difficult problem …
… because it isn’t easy “to wreck a nice beach”
"Why did Ken set the soggy net on top of his deck"
Notes: <number>

## Slide 12: MP3
Notes: <number>

## Slide 13: Audio Coding (MP3)
The MPEG committee chose to recommend 3 audio compression methods of increasing complexity and demands on processing power.
They are referred to as Audio Layer I, II and III.
  Layer I is the simplest, a sub-band coder with a psychoacoustic model.
  Layer II adds more advanced bit allocation techniques and greater accuracy. This is used for digital radio (DAB, Digital Audio Broadcast)
  Layer III (MP3) adds a hybrid filterbank and non- uniform quantization plus advanced features like Huffman coding, 18 times higher frequency resolution and bit reservoir technique.
Notes: <number>

## Slide 14: MP3 Coding
The standards require downward compatibility so, for example, a valid Layer III decoder must be able to decode any Layer I, II or III MPEG Audio stream. Similarly a layer II decoder should be able to decode Layer I and Layer II streams.
MPEG audio uses psychoacoustics models (perceptual coding), i.e., models of the way the human brain perceives sound.
  Humans can hear sounds with frequencies from about 20Hz to 20kHz.
  The masking effect: Imagine a loud tone with a frequency of 1000Hz and also a tone of say 1100Hz. The second tone will be ‘masked’ by the first 1000Hz tone. In general, any relatively weak sounds near louder sounds will be masked.
Notes: <number>

## Slide 15: Simple Masking Example (from http://www.digitalradiotech.co.uk)
The figure shows the threshold of hearing curve and a single tone (sinewave) with a frequency of 1kHz.
The red curve (A) is the normal hearing threshold
The green curve (B) is the masking curve due to the tone (C) and the band of noise in yellow (D) at 1.5kHz cannot be perceived by the human ear because of the masking effect of the tone at 1kHz.
Notes: <number>

## Slide 16: MP3 Coding … continued
Including a psychoacoustical model means that masked tones can be removed from the bitstream to improve compression performance.
The coder calculates masking effects by an iterative process until it runs out of time.
File sizes
  As we would expect, quality descriptors are difficult to match to file sizes or compression ratios. For example, different users, different applications, different codecs will all have different expectations, requirements or different results.
  But as a very rough guide ...
    higher quality bit rates would be128kps and from 224 - 320kps (closer to CD-quality).
    lower quality bit rates from 96kps and below.
Notes: <number>

## Slide 17: MP3 Demonstrations
Notes: <number>

## Slide 18: Summary
Speech and sound signals
  What signals look and sound like (SFS demo)
  Frequency components
  Low and high-pass filtering
  Compression approaches
Audio coding
  MP3 (perceptual coding)
  MP3 demonstrations (3 sample files each uncompressed, compressed and the difference)
Notes: <number>

## Slide 19
This concludes our introduction to speech and audio.
You can find course information, including slides and supporting resources, on-line on the course web page at
Thank
You
http://www.eee.bham.ac.uk/woolleysi/teaching/multimedia.htm
Notes: <number>