## Slide 1: Multimedia Data A Short Introduction to Colour and Colour Models
Dr Sandra I. Woolley
http://www.eee.bham.ac.uk/woolleysi
S.I.Woolley@bham.ac.uk
Electronic, Electrical and Computer Engineering
Notes: <number>

## Slide 2: A Short Introduction to Colour
The spectrum of light
The visible spectrum
Measuring and perceiving light and colour
Displaying colour
Colour models
Notes: <number>

## Slide 3: The Spectrum of Light
1666 : Sir Isaac Newton discovers the spectrum of light generated by sunlight passing through a glass prism.
We now know that visible light is composed of a relatively narrow band of frequencies in the electromagnetic energy spectrum (approx 400-700 Nanometers in wavelength).
The spectrum of light from regular tungsten and fluorescent bulbs is quite different from natural daylight.
In photography, white balancing is used to correct the effects of colour casts produced by artificial and non-ideal lighting conditions.
http://www.leefilters.com/lighting/advice/technical/
Notes: <number>

## Slide 4: The Visible Spectrum
The visible spectrum is part of the electromagnetic spectrum.
Light is composed of photons which display some of the properties of a wave and some of the properties of a particle. This is wave-particle duality; a concept central to quantum physics.
The standardised (CIE) wavelengths are
  700nm for red,
  526.1nm for green
  and 435.8nm for blue.
(Wavelength image from Universe by Freedman and Kaufmann.)
Notes: <number>

## Slide 5: Light Primaries
The primary colours of light (pictured top) can be added to produce white light and the secondary colours
  magenta = red + blue
  cyan = blue + green
  yellow = red + green
The secondary colours are pigment colours used in printing. They are colours which absorb a primary colour of light and reflect the other two.
Combining the 3 secondary pigment colours produces black.
Notes: <number>

## Slide 6: Perception of Colour
We humans have “tristimulus” colour vision that uses three different types of colour sensing cones, sensitive to longer, medium and shorter visible wavelengths.
Our cone types are sometimes referred to as red, green and blue. But their peak sensitivities do not exactly match these colours.
Only about 2% of the cones are sensitive to blue wavelengths. Our maximum sensitivity is in the yellow-green range. The eye can detect more shades of green than any other colour.
http://personales.upv.es/gbenet/teoria%20del%20color/water_color/color1.html
Notes: <number>

## Slide 7: Light Measures
Luminance – is a measure of the density of light intensity in a given direction.
Brightness – is a measure of luminance perception.
Pleasanton Fire Department Station Number Six light bulb has been
burning since 1901.
Considered the longest-burning bulb in the world. It is a hand-blown bulb with a carbon filament. www.centennialbulb.org
Notes: <number>

## Slide 8: Light Measures
White's illusion is an optical illusion illustrating the fact that the same target luminance can elicit different perceptions of brightness in different contexts.
Television screens depend on this visual illusion. Pixels that are not illuminated are seen as black, when they are really the same dim grey seen when the television is turned off.
A more extreme example is an overhead projector screen, which is bright white in reality but whose less-illuminated regions appear black.
http://en.wikipedia.org/wiki/White%27s_illusion
http://web.mit.edu/persci/gaz/gaz-teaching/flash/white-movie.swf
More interesting flash illusions http://web.mit.edu/persci/gaz/gaz-teaching/index.html
White’s Illusion
Notes: <number>

## Slide 9: Distinguishing between Colours
Colours are generally distinguished by :-
  brightness - subjective measure of chromatic intensity
  hue - associated with the dominant wavelength (the perceived colour)
  saturation - relative purity (amount of pure hue e.g., saturation =0 for white).
  For example, in the ‘HSV’ colour model saturation is defined as
http://flickr.com/photos/flopper/378433798/
Notes: <number>

## Slide 10: Displaying Colour
In colour LCD displays each individual pixel is divided into three cells, or subpixels, which are coloured red, green, and blue
Each subpixel can be controlled independently to yield thousands or millions of possible colours for each pixel.
The additive effect being received by the eye as full-colour.
30 successive images per second in all 3 colours completes the illusion of continuous full colour images.
http://electronics.howstuffworks.com/lcd5.htm
http://www.pclaptop-review.com/wp-content/uploads/2006/11/B000HAR8UI.01._SS500_SCLZZZZZZZ_V39088043_.jpg
Notes: <number>

## Slide 11: Metamerism
Metamerism is the phenomenon where two colour samples with different spectra appear to be the same colour.
As we have seen, the human eye contains only three colour receptors (cones), which means all colours are reduced to three sensory tristimulus quantities.
Metamerism occurs because each type of cone responds to the cumulative energy from a range of wavelengths, so that different combinations of light across all wavelengths can produce equivalent receptor responses and hence the same colour perception.
Two spectrally different colour samples that visually match are called metamers.
Variation in lighting conditions also affects colour perception. For example, two items can appear the same colour in artificial lighting but be patently different in natural light.
http://en.wikipedia.org/wiki/Metamerism_%28color%29
An example of metamerism from variant lighting from photoshopnews.com
Notes: <number>

## Slide 12: Colour Models
Notes: <number>

## Slide 13: The RGB Colour Model
A colour model is an abstract mathematical model that provides a way of describing colours as coordinates. Usually as 3 colour components.
The simplest colour model is the RGB model (Red, Green, Blue model).
Here we can represent any colour as a combination (set of coordinates) describing a position in the 3D colour space.
Notes: <number>

## Slide 14: CMY and CMYK Colour Models
The CMY and CMYK colour models are commonly used in printing
The letters refer to Cyan, Magenta, Yellow and blacK.
The addition of black is useful in printing where C+M+Y alone can produce an imperfect black.
http://en.wikipedia.org/wiki/CMYK_color_model
Notes: <number>

## Slide 15: The YUV Colour Model
YUV is the colour encoding system used for analogue television (NTSC, PAL and SECAM).
Y represents* luminance (originally Y’ and “luma”) and U and V are chrominance channels.
V represents R-Y and U represents B-Y
More accurately:
Y= 0.299 R + 0.587 G + 0.114 B
U= 0.564 (B - Y) + 128
= -0.169 R - 0.332 G + 0.500 B + 128
V= 0.713 (R - Y) + 128
= 0.500 R - 0.419 G - 0.0813 B + 128
*It is more strictly Y’ which distinguishes it from CIE-defined luminance, however, in practice it is more casually referred to simply as luminance http://www.poynton.com/PDFs/YUV_and_luminance_harmful.pdf
Notes: <number>

## Slide 16: The YCbCr Colour Model
YCbCr - Another coordinate system. It is commonly used for digital images and video (e.g., JPEG and MPEG).
The JPEG File Format* lists the 8-bit YCbCr model
Y = 0.299 R + 0.587 G + 0.114 B
Cb = - 0.1687 R - 0.3313 G + 0.5 B + 128
Cr = 0.5 R - 0.4187 G - 0.0813 B + 128
Colour space conversion is often required (see Matlab Color Space Converter right).
For example, To convert back to RGB from YCbCr (8-bit) we need to calculate:
R = Y + 1.402 (Cr-128)
G = Y - 0.34414 (Cb-128) - 0.71414 (Cr-128)
B = Y + 1.772 (Cb-128)
*http://www.jpeg.org/public/jfif.pdf
http://www.mathworks.com/matlabcentral/fileexchange/loadFile.do?objectId=7744
Notes: <number>

## Slide 17: The CIE Colour Models
CIELAB was one of the first mathematically defined colour spaces.
It is the most complete colour model used to describe all the colours visible to the human eye.
It is a 3-dimensional model based on luminance (L) and two colour channels (A and B)
It was based on an early standard (CIE 1931) shown on the right. Here the outside edge plots all the pure colours of the spectrum.
http://en.wikipedia.org/wiki/CIE_1931_color_space
Notes: <number>

## Slide 18: The CIE Colour Model
The CIE model is often used to specify ranges of colours that can be produced by a particular source. This range is referred to as a gamut.
For example, a typical computer monitor has a colour gamut much smaller than the set of all possible colours.
As we have seen a display can produce colour by mixing red, green, and blue colours.
Shown on the right inside the triangle is an example of an RGB colour gamut produced by a colour monitor.
http://www.ncsu.edu/scivis/lessons/colormodels/color_models2.html
Notes: <number>

## Slide 19: The HSV Colour Model
The HSV colour model is a simple colour model that more perceptually defines colour relationships. This model is often preferred by artists.
The HSV values are Hue, Saturation and Value.
S=0 represents white. V=0 represents black.
V=S=1 (or 100%) represents the pure colours around the top of the cone.
Hue is represented by its angular position.
The HSV colour wheel model is often used in computer graphics applications when user colour selection is required.
The hue is represented by a circular region and a separate triangular region is used to represent saturation and value.
HSL is a similarly simple perceptual colour model that represents colour as Hue, Saturation and Lightness.
http://en.wikipedia.org/wiki/HSV_color_space
Notes: <number>

## Slide 20: Summary
That concludes our short introduction to colour and colour models.
The spectrum of light
The visible spectrum
Measuring and perceiving light and colour
Displaying colour
Colour models
Notes: <number>

## Slide 21
This concludes our introduction to colour.
You can find course information, including slides and supporting resources, on-line on the course web page at
Thank
You
http://www.eee.bham.ac.uk/woolleysi/teaching/multimedia.htm
Notes: <number>