## Slide 1: Introduction to Energy Engineering
Course Introduction
Dr Mike Spann
School of EECE
m.spann@bham.ac.uk

## Slide 2: Course Outline
This is an introductory course teaching you some basic stuff about:
  Where our energy comes from
  How electricity is produced
  Renewable and non-renewable energy
  Climate change and global warming
  How our energy future is looking

## Slide 3: Course Outline
These lectures are ‘interest only’ as assessment is by group assignment (discussed later)
  So no exam!
Pre-requisite knowledge?
  Some basic knowledge of physics (I’m a physicist!)
    Conservation of energy is a good starting point!

## Slide 4: Course Outline
2 lectures spanning 3 double lecture sessions in this time slot.
  Lecture 1: Earth’s Energy Budget and Global Energy Resources
  Lecture 2: Electrical Energy Generation and Future Energy Challenges

## Slide 5: Course Resources
Your first port of call should be the course Canvas page for lecture material and any supporting material
  https://canvas.bham.ac.uk/login
There is no set text book as most of the material is sourced online but I will update the Canvas page with references
  However, if you want a great bedtime read, try ‘Sustainable Energy – Without the Hot Air’ by David MacKay
A very good online resource discussing the Earth’s energy balance is:
  Climate and Earth’s Energy Budget by Rebecca Lindsey, Earth Observatory, NASA Goddard Space Flight Center, January 14, 2009
http://earthobservatory.nasa.gov/Features/EnergyBalance/

## Slide 6: Lecture 1
  Earth’s Energy Budget and Global Energy Resources

## Slide 7: Part I
  Earth’s Energy Budget

## Slide 8: Introduction
Where do Earth’s natural resources come from?
  Fossil fuels
  Uranium
  Solar energy
  Wind Energy
  Tidal energy
  etc
Most are driven ultimately by solar radiation
On Earth there is a complex interaction between sub-systems involving oceans, cloud, land, volcanoes, plants, animals, etc
  So called ‘natural cycles’
  Although man has intervened somewhat to disrupt these
Scientists define specific cycles to model flows between sub-systems, for example
  Carbon cycle
  Hydrological (water cycle)

## Slide 10
Hydrological Cycle

## Slide 11: Earths Energy Budget
The sun is responsible for most of the Earth’s energy resources
The surface of the Sun has a temperature of about 5,800K
At that temperature, most of the energy the Sun radiates is visible and near-infrared light
The Earth is in ‘energy balance’
  That’s why it maintains a roughly constant temperature of about 288K
  The sun’s (short-wave) radiation impacting on Earth is balanced by the thermal (longwave) radiation emitted by Earth

## Slide 12: Some basic physics
Hot bodies (or any body with a temperature above zero degrees Kelvin) emits electro-magnetic radiation
  This is propagated as a transverse wave
  Waves are defined by their speed (c), wavelength l, and frequency n
  Frequency and wavelength are inversely related
c = ln
c = 3.8 x 108 m/s

## Slide 13: Some basic physics
The ‘electro-magnetic’ spectrum gives different names to these EM waves according to their wavelength (or frequency/energy)
  For example visible light has a wavelength between 0.4 and 0.7μm
  X rays and gamma rays have much shorter wavelength and hence higher frequency/energy explaining why they are more dangerous
E = hn
h is Planck’s constant (6.62606957 × 10-34 m2 kg / s)

## Slide 14: Power and Energy
A word on units:
  Energy is expressed as Joules (J) – measures heat, electricity and mechanical work
    The Joule is the SI unit of energy
      1 kg m2 s-2
    1 Joule is a tiny unit of energy which is why it’s almost always prefixed with M(106), G(109) ……
  There are some other more exotic units for energy which are often used in the energy business
    For example the British thermal unit (Btu) is the energy to raise 1 lb of water 1ºF
      1 Btu ≈ 1kJ

## Slide 15
Power and Energy
The BTU (British Thermal Unit) is often used and in particular the quadrillion (1015) BTU which is about 1 exajoule (1018)
  Total world energy consumption is around 500 exajoules (2010) which is roughly 500 quadrillion BTU!
We can easily convert between different units
  joule = 9.48×10−4 BTU
  1 boe (barrel of oil equivalent) = 5.45 x 106 BTU
  1 toe (ton of oil equivalent) = 39.7 x 106 BTU
  1 cubic feet of natural gas = 983 BTU
  1 metric ton of coal = 22.72 * 106 BTU
  1 exajoule = 174 million boe’s

## Slide 16
Power and Energy
We can get a reasonable idea about our annual energy use per capita by using the boe (barrel of oil equivalent unit)
  The UK ranks about 15th in the world with an average annual per capita energy consumption of around 150 million BTU’s
    Approximately 30 barrels of oil equivalent!
    By contrast, average consumption is about 6 barrels in the developing world

## Slide 17
Power and Energy
Power is the flow of energy
A good analogy is to compare it with fluid flow
A useful unit of energy is the kilowatt-hour
  That’s the energy delivered by a power source of 1kW in 1 hour
  It’s equal to 1000 x 3600 J = 3.6MJ
  Quite often people refer to average energy consumption (for example kWh per day) which is a power
Energy (kWh) | Power (kW)
Volume (litres) | Flow (litres/second)
energy = power x time
volume = flow x time

## Slide 18
Energy and Entropy
Is all energy the same?
  Yes and no!
    Yes
      In the sense of energy conservation
    No
      In the sense of useful (low entropy) and less useful (high entropy) energy
Entropy is the amount of disorder (randomness) in a system
  Highly disordered = High entropy
  Entropy always increases meaning systems get more disordered
    A wall of bricks will collapse
    An ice cube melts
    A dye will diffuse in a liquid

## Slide 19
Energy and Entropy
So we can distinguish different grades of energy
Electrical, chemical, mechanical and nuclear energy are all useful forms
Thermal energy (especially in tepid things) is less useful
  Your can use electrical energy to run your TV or convert it to heat to boil a kettle
  You can’t do either with a tepid bath full of water
Often the energy ‘grade’ is reflected in the units kWh(e) – electrical and kWh(th) – thermal
Conversion between energy grades incurs losses usually as thermal
  Burning chemical energy (oil) to produce electrical energy is about 40% efficient
  The food chain is essentially a chain of increasing entropy!
  A steam turbine needs a low temperature (condenser) to ‘dump’ entropy

## Slide 20: Some basic physics (cont)
The amount of heat energy reaching the Earth’s surface (measured in watts per square metre) depends on 3 things
  The energy flux
  The sun’s temperature
  The distance to the sun
(Obviously there are other factors such as the amount of reflection in the upper atmosphere)

## Slide 21: Some basic physics
Energy flux is how much energy (or any material) passes through a unit surface area per unit time
  Units: W/m2
  J/m2/s

## Slide 22: Some basic physics
The angle of the impacted earth’s surface to the sun affects the flux
Clearly the flux depends on the latitude
Nearer the equator – higher flux
  More watts per square metre
Polar regions cooler due to lower energy flux

## Slide 23: Some basic physics
Flux also depends on distance of an object or observer from the object emitting the radiant energy
  Flux of solar energy decreases with distance from the sun
  Relationship is an inverse-square law

## Slide 24: Solar Radiation
All matter in the universe that has a temperature above absolute zero radiates energy across a range of wavelengths in the electromagnetic spectrum
The hotter something is, the shorter its peak wavelength of radiated energy is
  The hottest objects in the universe radiate mostly gamma rays and x-rays
  Cooler objects emit mostly longer-wavelength radiation, including visible light, thermal infrared, radio, and microwaves

## Slide 25: Solar Radiation
Wien’s law describes mathematically the amount of radiation emitted from hot bodies
  These bodies are assumed ‘black’ bodies
    Perfect absorbers and emitters in thermal equilibrium
    The radiation emitted by the sun and planets are good approximations to black body radiation

## Slide 26: Solar Radiation
The sun and Earth both are ‘hot’ bodies
  Because the sun is much hotter, its emissions (measured as energy flux) are at a much shorter wavelength according to Wien’s law
  Earth emits relatively long wave radiation (in the IR band)
UV Vis IR (heat)

## Slide 27: Solar Radiation
Wien’s law is quite complicated as it describes the energy ‘density’ distribution
  Energy density is the amount of energy per unit wavelength or frequency
Wilhelm Wein derived it in 1893 based on thermodynamics
  It is only an approximation and was later superseded by Planck’s law which is a better approximation over range of wavelengths
I is the energy per unit time per unit frequency per unit solid angle per unit area!
  k is Boltzmann’s constant
  c is the speed of light
  h is Planck’s constant
  T is the temperature
  v is the frequency

## Slide 28: Solar Radiation
The main application of this formula is in deriving Wien’s displacement law
  This is the wavelength giving the maximum radiative energy at a certain temperature
  In other words, can we measure the temperature of a star (or the sun) from it’s emission!
We need some maths to derive the wavelength at which the energy emitted is maximum
  Here are the main details. I will leave you to fill in the gaps 

## Slide 29: Solar Radiation
There is an inverse relationship between the wavelength of the peak of the emission of a black body and it’s temperature
  This is the wavelength giving the maximum radiative energy at a certain temperature
This is an important relationship in areas such as astrophysics and plasma physics
Examples:
  A wood fire at 1500 K puts out peak radiation at 2.9 x 10-3/1500 ≈2 μm. This is far more energy in the infrared than in the visible band, which ends about 0.7μm
  Mammals at roughly 300 K emit peak radiation at about 10 μm, in the far infrared
    Hence the use of thermal imaging cameras
  The effective temperature of the Sun is 5778 K. This corresponds to a peak emission at a wavelength of around 5 μm. This is the wavelength of green light

## Slide 30: Solar Radiation
An alternative formulation of Wien’s law can be obtained by integrating I(v,T) over all frequencies to get the total energy radiated as a function of temperature
  Quite advanced calculus required
  The result is the Stefan-Boltzmann law and is a very simple relationship
E = σT4
E is the radiant heat energy emitted from a unit area in one second and T is the absolute temperature (in degrees K)
σ Stefan-Boltzmann constant (5.67 x 10-8 J s-1 m-2 K-4)
  It’s not actually a new constant of nature as it’s expressed in terms of other physical constants

## Slide 31: Solar Radiation
What all this amounts to is that at Earth’s average distance from the Sun (about 150 million kilometres), the intensity of solar energy reaching the top of the atmosphere directly facing the Sun is about 1,360 watts per square meter
  This is often known as the total solar irradiance or sometimes the insolation
You could run a refrigerator all day with the total solar irradiance falling on 1 square metre in 1 hour
It’s important to understand that this is a maximum
  For example this assumes that the radiation hits the surface perpendicularly (maximum flux)
  Also the value varies significantly with time of day and latitude
  Averaged over the entire planet, the amount of sunlight arriving at the top of Earth’s atmosphere is only 1/4 of the total solar irradiance, or approximately 340 watts per square meter

## Slide 32: Earth’s Energy Balance
If Earth’s temperature is constant, the planet has to be in radiative balance
Many complex processes are at work to maintain a constant temperature and these are responsible (amongst other things) for our climate
  However, the physical principles at work are basically simple mechanisms of heat transfer
    Radiation
    Conduction
    Convection
    Latent heat

## Slide 33: Earth’s Energy Balance
Only around 50% of incoming solar radiation gets through the atmosphere to the Earth’s surface
  Around 70% of the radiation is absorbed by Earth and ultimately returned to space as IR
  Energy input = energy output

## Slide 34: Earth’s Energy Balance
There must be an energy balance for the 48% of radiation reaching Earth’s surface
This is emitted through evaporation (25%)
  Latent heat
Convection (5%)
  Heated warm air rising causing air currents
Radiation (17%)
  Thermal infrared energy (heat) radiated by atoms and molecules on the surface

## Slide 35: Earth’s Energy Balance
We can work out an energy balance also for Earth’s atmosphere which demonstrates the natural greenhouse effect
  Satellite measurements indicate that the atmosphere radiates thermal infrared energy equivalent to 59% of the incoming solar energy
  Clouds, aerosols, water vapour, and ozone directly absorb 23% of incoming solar energy
  Evaporation and convection transfer 25% and 5% of incoming solar energy from the surface to the atmosphere totalling the equivalent of 53% of the incoming solar energy to the atmosphere
  The remaining 5-6% comes from the Earth’s surface
    Absorbed by greenhouse gases, these greenhouse gas molecules radiate heat in all directions, some of it spreads downward and ultimately comes back into contact with the Earth’s surface, where it is absorbed – ‘natural greenhouse’ effect

## Slide 36: Earth’s Energy Balance
The ‘natural’ greenhouse effect is essential to support life
  Major role in warming atmosphere
  Traps heat
  Without greenhouse gases, planet would be much colder (~ -20oC)
Note that ‘greenhouse’ is an unfortunate term
  Real greenhouses suppress convection through the glass whereas the ‘greenhouse effect’ is all about radiated heat

## Slide 37: Earth’s Energy Balance
Incidentally, this explains the importance of the O3 layer
  Absorption takes place in the O3 layer
  A depleted O3 layer is very harmful to humans
  The size of the Antarctic ozone hole reached 11.1 million square miles on September 24, 2003, slightly larger than the North American continent
  Check out Nasa’s ozone watch web site for up to date animations
    http://ozonewatch.gsfc.nasa.gov/

## Slide 38: Earth’s Energy Balance
It’s worth mentioning the man-made greenhouse effect
About 17% of incoming solar radiation is radiated by Earth’s surface
  Of this, 12% escapes into space and 5-6% is captured by greenhouse gases and re-radiated in all directions
  This is a fine energy balance which keeps a stable temperature on Earth
There are many man made phenomena which effect this energy balance and hence Earth’s surface temperature
  Pollution (aerosols), which absorb and reflect incoming sunlight
  Deforestation, which changes how the surface reflects and absorbs sunlight
  The rising concentration of atmospheric carbon dioxide and other greenhouse gases, which decrease heat radiated to space

## Slide 39: Earth’s Energy Balance
Effectively the energy imbalance changes the temperature
  However, remember the Stefan-Boltzmann law
  Changes in temperature are negligible because of the 4th power
  Global average surface temperature has risen between 0.6 and 0.9K in the past century
  The concern is continued and increasing concentrations of greenhouse gases
Man made reduction 12% -> ~11%
E = σT4

## Slide 40
CO2 Emissions and Climate Change
Global warming will impact our weather patterns, affect global ecosystems, cause rising sea levels (as is happening already) leading to coastal low lying areas and impact large numbers of people
Since 1993, NASA satellites have shown that sea levels are rising more quickly, about 3 millimetres per year, for a total sea level rise of 48 millimetres between 1993 and 2009
https://www.youtube.com/watch?feature=player_embedded&v=ab6jV4VBWZE

## Slide 41
CO2 Emissions and Climate Change
Global warming – fact or myth?
  There is much debate about the extent of global warming both from serious scientists as well as vested interests
  No one doubts that we are pumping carbon dioxide into the atmosphere at increasing rates
    The world added roughly 100 billion tonnes of carbon to the atmosphere between 2000 and 2010 mainly through burning fossil fuels. That is about a quarter of all the CO₂ put there by humanity since 1750
  No one doubts that CO₂ is a greenhouse gas
    This is easily shown in the laboratory
  However, there is a doubt as to how much the planet will be warmed
    The five-year mean global temperature has been flat for a decade which is still a mystery which climate scientists are struggling to explain
    Predictive models are complex and must involve factors such as clouds and aerosols as well as feedback systems

## Slide 42
CO2 Emissions and Climate Change
There are ‘myth-mongerers’ and ‘myth-debunkers’ amongst both amateur scientists, commentators and serious scientists alike
The main battleground is that the effect of ‘man’ on climate change is insignificant compared to the huge natural effects of the oceans, polar regions and the atmosphere
  Here is an alternative view from the Friends of Science which is a non-profit organization based in Canada
https://www.youtube.com/watch?v=KnipKZAhgW4&feature=player_embedded

## Slide 43: Part II
  Global Energy Resources

## Slide 44
Obviously the first distinction is into renewable and non-renewable
  A nonrenewable resource is a natural resource that cannot be re-made or re-grown at a scale comparable to its consumption
  Renewable resources are natural resources that can be replenished in a short period of time
  Sustainable???
Global Energy Resources

## Slide 45
We are all familiar with examples of each
  A nonrenewable resource is a natural resource that cannot be re-made or re-grown at a scale comparable to its consumption
  Nonrenewable
    Coal
    Oil
    Gas
    Nuclear
  Renewable
    Solar
    Wind
    Water (Hydro-electric, wave)
    Biomass
    Geothermal
Global Energy Resources

## Slide 46
Coal, Oil and Gas are often called "fossil fuels" because they have been formed from the fossilized remains of prehistoric plants and animals
They are made of a mixture of different hydrocarbons
Oil and gas have the same origin
  Decaying microscopic marine life
  When the plankton dies, it forms an organic mush on the sea bed
  Under anaerobic conditions (when there is no oxygen) other animal life to feed on the plankton can’t be supported and the mush accumulates
Oil and Gas
Plant plankton
Animal plankton

## Slide 47
When sediment (the sea bed) contains more than 5% organic matter, it is called black shale and it is the pre-curser to hydrocarbon reserves
As black shale is buried, it comes under more pressure so it is heated
The depth (and hence temperature of heating) determines if it ultimately becomes kerogen
As kerogen is heated further, it releases oil and gas
Shales rich in kerogens that have not been heated to a warmer temperature to release their hydrocarbons may produce oil shale deposits
Oil and Gas
Black shale deposits

## Slide 48
Around 90°C, it is changed into the liquid state, which we call oil
Around 150°C, it is changed into gas
A rock that has produced oil and gas in this way is known as a source rock
The last stage of the process is the hydrocarbons permeating up through the rock to form reservoirs
Some rocks are permeable and allow oil and gas to freely but others are impermeable and block the upward passage of oil and gas
Where oil and gas rises up into a dome (or anticline) capped by impermeable rocks it can’t escape
  Seismic surveys are used to locate likely rock structures underground in which oil and gas might be found
  Dome like structures are a good indication of hydrocarbon reserves
Oil and Gas
Drill here!

## Slide 49
Coal currently provides about 30% of the total UK energy production (with gas at around 40%)
Now that oil and gas are dwindling, many energy producers and users are looking again at the potential of coal
Unlike oil and gas, coal is not formed from marine organisms, but from the remains of land plants
A swampy setting, in which plant growth is lush and where there is water to cover fallen trees, dead leaves and other plant debris, is ideal for the initial stages to create coal
Coal

## Slide 50
The formation of coal from dead plant matter requires burial, pressure, heat and time
The process works best under anaerobic conditions (no oxygen) since the reaction with oxygen during decay destroys the organic matter
It is the carbon content of the coal that supplies most of its heating value
The greater the carbon to oxygen ratio the harder the coal, the more potential energy it contains
Over time there are different stages to coal deposit formation
Coal

## Slide 51
Coal
The products of coalification are divided into four major categories based on the carbon content of the material
  Peat
  Lignite
  Bituminous
  Anthracite
Peat is an accumulation of partially decayed vegetation matter and is the first stage in the formation of coal
Peat forms in wetlands
It contains a large amount of water and must be dried before use
Historically, it has been used as a source of heat and burns with a long flame and considerable smoke

## Slide 52
Coal
Lignite is the second step in the formation of coal and is formed when peat is subjected to increased vertical pressure from accumulating sediments
Lignite, often referred to as brown coal, is the lowest rank of coal and used almost exclusively as fuel for steam-electric power generation. It’s inefficient to transport and often burn in power stations close to the mines
Bituminous coal is the third stage of coal formation
Additional pressure over time has made it compact and virtually all traces of plant life have disappeared
It is of higher quality than lignite coal but of poorer quality than anthracite coal
It is greatly used in industry as a source of heat energy
It has a high inherent moisture content, sometimes as high as 66 percent, and very high ash content compared to bituminous coal
Because of its low energy density, it is inefficient to transport and it is often burned in power stations constructed very close to the mines
The Latrobe Valley in the state of Victoria, Australia contains estimated reserves of some 65 billion tonnes of brown coal The deposit is equivalent to 25% of known world reserves
Lignite
Bituminous coal

## Slide 53
Coal
Anthracite is formed during the forth stage of coal formation
It is the most valuable and highest grade of coal, and has a carbon content
It burns far more efficiently with less smoke
The principal use of anthracite is for a domestic fuel It delivers high energy per its weight and burns cleanly with little soot but it’s prohibitively expensive to use in power stations
As the coals becomes harder, their carbon content increases, and so does the amount of heat released
  Anthracite produces twice the energy (BTUs) of lignite

## Slide 54
Pro’s and Con’s of Fossil Fuels
Pro’s
  Transporting coal, oil and gas to the power stations is easy
  Fossil fuels are cheap and reliable sources of energy. They are excellent types of fuel to use for the energy base-load, as opposed to some of the more unreliable energy sources such as wind and solar energy
Con’s
  Basically, the main drawback of fossil fuels is pollution
  Coal is by far the worst pollutant and has the highest carbon density
  Burning any fossil fuel produces carbon dioxide, which contributes to the "greenhouse effect", warming the Earth.
  Burning coal produces sulphur dioxide, a gas that contributes to acid rain.
  Mining coal can be difficult and dangerous. Strip mining destroys large areas of the landscape

## Slide 55
So how much fossil fuel is left?
We can get an estimate of this by dividing the ‘known recoverable’ resources by the rate of usage
The figure can change because of
  Increased conservation
  New discoveries
  Better technologies leading to more efficient electricity production
  Existing known reserves will become more profitable as the supply dwindles leading to more exploitation

## Slide 56
So how much fossil fuel is left?
Oil
  1,300 billion barrels of proven reserves still in the ground, worldwide
  At current rates of consumption, 87 million barrels a day, oil will run out in roughly 41 years
Gas
  6,400 trillion cubic feet of natural gas reserves around the world about the same as having 1,140 billion barrels of oil (BOE), in terms of its energy content
  The world is consuming roughly 53 million barrels of oil equivalent (BOE) of natural gas every day. At that rate gas will run out in 59 years
Coal
  Worldwide, there is roughly 3,100 billion BOE of coal
  Consumption is 71 million BOE of coal a day so we have 120 years' supply of coal left
Chart: Number of years
| Oil | Gas | Coal
Series 1 | 41 | 59 | 120
Series 2
Column1

## Slide 57
So how much fossil fuel is left?
Don’t panic!
  Existing and new resources will expand to fill the gap
    Nuclear power will expand
    Existing fossil fuel technologies such as fracking to extract shale gas will come on stream
      Shale gas already constitutes 20% of US gas reserves
      But controversial
    Also carbon capture technology may lengthen the lifespan of coal
    Massive expansion of renewable energy sources are planned
Think of it as an opportunity 

## Slide 58
Uranium
Uranium is the basis of nuclear power which currently produces about 17% of the world’s electricity needs
Uranium is one of the more common elements in the Earth's crust and it can be found almost everywhere in rock, soil, rivers, and oceans
Uranium ore is processed near the mine to produce “yellow cake”, a material rich in U3O8
  200 tons of this are needed per year for a 1GW nuclear power plant
Only 0.7% of U in yellow cake is 235U. Most of the rest is 238U which does not work for fission power
  There is a huge amount of processing to convert yellow cake to useable nuclear fuel
Whilst some reactors run on unenriched uranium, in most cases it must be enriched so it contains about 5% 235U

## Slide 59
Uranium
How long will our uranium reserves last?
Most current nuclear reactors are light water reactors (LWRs) which use low enriched uranium (LEU)
There are about 400 civil nuclear power plants currently operating in the world and each requires about 200 metric tons of uranium to operate per year
  So present-day reactors require about 80,000 metric tons of natural uranium a year
Identified uranium resources total 5.5 million metric tons, and an additional 10.5 million metric tons remain undiscovered—a roughly 200-year supply at today's consumption rate in total
Chart: Number of years
| Oil | Gas | Coal | Uranium
Series 1 | 41 | 59 | 120 | 200
Series 2
Column1

## Slide 60
Uranium
Likely to be an underestimate
  Developments in technology could reduce the uranium needs of LWRs by as much as 30 percent per metric ton of LEU
  Development of fuel-recycling fast-breeder reactors, which generate more fuel than they consume, would use less than 1 percent of the uranium needed for current LWRs. Breeder reactors could match today's nuclear output for 30,000 years
  Extraction of uranium from seawater would make available 4.5 billion metric tons of uranium—a 60,000-year supply at present rates
  Thorium?? Far more abundant than uranium
Nuclear power is likely to be a significant contributor to our energy needs within a few decades
Chart: Number of years
| Oil | Gas | Coal | Uranium
Series 1 | 41 | 59 | 120 | 1000
Series 2
Column1

## Slide 61
Renewable Energy Resources
We will briefly look at renewable energy resources although in theory these are infinite by definition
  Limitations only come about because of lack of economic viability or technical restrictions
  We will look in more detail about how energy is produced from these resources later
  There’s no doubt that these will play an increasing role in our energy supply over the next few decades

## Slide 62
Solar Energy
Solar power comes from thermonuclear reactions in the sun and is the ‘ultimate’ renewable energy source
We have seen that around 48% of the sun’s energy is absorbed at Earth’s surface
  Only this is useable
The potential for exploitation of this resource is massive
  The amount of solar energy that reaches the Earth’s surface every hour is greater than humankind’s total demand for energy in one year
There are 2 main principles to exploit solar power
  Direct heating
  Photovoltaic cells

## Slide 63
Solar Energy
We measure the potential for a location to be suitable for solar energy generation by the amount of insolation
  Insolation is the total amount of solar radiation energy received on a given surface area during a given time
  It is also called solar irradiation and expressed as "hourly irradiation" if recorded during an hour or "daily irradiation" if recorded during a day
  The unit is the megajoule per square metre (MJ/m2) or joule per square millimetre (J/mm2)
  Practitioners in the business of solar energy may use the unit watt-hour per square metre (Wh/m2)
  The average solar radiation arriving at the top of Earth’s atmosphere is 1366W/m2 but the amount arriving at the surface is a fraction of this
Top of atmosphere
Surface

## Slide 64
Solar Energy
The UK's insolation is around 2.9 kWh/m²/day — a fraction of that in southern Europe and North Africa
Even so, 1,000 km2 (10% of the area of Scotland), where the insolation is about 900 kWh/m²/year would provide 180,000 GWh/year, equal to all of Scotland's energy demand
  Since most of that would be in the summer, when Scotland receives 12–14 hours of sun, the excess would need to be stored or exported

## Slide 65
Wave Energy
Among other types of renewable energy, oceans contain energy in the form of waves and tidal currents
Differential warming of the earth causes pressure differences in the atmosphere, which generate winds
As winds move across the surface of open bodies of water, they transfer some of their energy to the water and create waves
The amount of energy transferred and the size of the resulting wave depend on
  the wind speed
  the length of time for which the wind blows
  the distance over which the wind blows
Therefore, coasts that have exposure to the prevailing wind direction and that face long expanses of open ocean have the greatest wave energy levels

## Slide 66
Wave Energy
The best wave resources occur in areas where strong winds have travelled over long distances
The best wave resources in Europe occur along the western coasts which lie at the end of a long fetch (the Atlantic Ocean)
Nearer the coastline, wave energy decreases due to friction with the seabed, therefore waves in deeper, well exposed waters offshore will have the greatest energy
There are 2 basic principle that designs exploit
  A change of water level by tide or wave can move or raise a float, producing linear motion from sinusoidal motion
  Water current can turn a turbine to yield rotational mechanical energy to drive a pump or generator

## Slide 67
Tidal Energy
Tidal streams are created by the constantly changing gravitational pull of the moon and sun on the world’s oceans
Tidal stream technologies capture the kinetic energy of the currents flowing in and out of the tidal areas
Since the relative positions of the sun and moon can be predicted with complete accuracy, so can the resultant tide. It is this predictability that makes tidal energy such a valuable resource
Tidal stream resources are generally largest in areas where a good tidal range exists, and where the speed of the currents are amplified by the funnelling effect of the local coastline and seabed, for example, in narrow straits and inlets, around headlands, and in channels between islands

## Slide 68
Hydro-Electric Energy
Hydropower energy is ultimately derived from the sun, which drives the water cycle
  Rivers are recharged in a continuous cycle. Because of the force of gravity, water flows from high points to low points
  There is kinetic energy embodied in the flow of water

## Slide 69
Hydro-Electric Energy
Man-made dams create a large difference in height and hence in potential energy between the reservoir and the run-of area
  The flow of water through sluice gates can be controlled by valves
  This controls the power output
Since hydroelectric dams do not burn fossil fuels, they do not directly produce carbon dioxide
  While some carbon dioxide is produced during manufacture and construction of the project, this is a tiny fraction of the operating emissions of equivalent fossil-fuel electricity generation
  Reservoirs created by hydroelectric schemes often provide facilities for water sports, and farming fish in the reservoirs is common

## Slide 70
Hydro-Electric Energy
In the UK hydropower has had some renewed interest because of UK and EU targets for reductions in carbon emissions
Typical sites for hydropower projects tend to be in remote areas including areas of outstanding beauty so possibilities for development are limited
  So called ‘run of the river’ schemes use the flow of the river to drive turbines and require little storage
  Less impact to the environment as no dams are required
The Dinorwig power station in North Wales is a 1,800 MW pumped-storage hydroelectric scheme, in north Wales, and the largest hydroelectric power station in the UK

## Slide 71
Geothermal Energy
Geothermal energy is a renewable source
It is energy ‘stored’ in Earth usually at great depth
70% comes from the decay of radioactive nuclei with long half lives that are embedded within the Earth
Some energy is from residual heat left over from Earths formation
The rest of the energy comes from meteorite impacts

## Slide 72
Geothermal Energy
On average, the Earth emits 1/16 W/m2. However, this number can be much higher in areas such as regions near volcanoes, hot springs and fumaroles
As a rough rule, 1 km3 of hot rock cooled by 1000C will yield 30 MW of electricity over thirty years
It is estimated that the world could produce 600,000 EJ over 5 million years
There is believed to be enough heat radiating from the center of the Earth to fulfill human energy demands for the remainder of the biosphere’s lifetime
Geothermal production of energy is 3rd highest among renewable energies. It is behind hydro and biomass, but before solar and wind
  For example Iceland is one of the more countries successful in using geothermal energy where 86% of their space heating and 16% of their electricity generation uses geothermal energy

## Slide 73
Wind Energy
Wind energy is essentially a limitless and inexhaustible resource
Differential heating of the earth’s surface and atmosphere induces vertical and horizontal air currents that are effected by Earth’s rotation and contours of the land -> WIND
There is enough power in the wind blowing at any one time on Earth to provide all of our energy needs
  The practical problems are of building enough wind turbines and finding the area to put them to harness it

## Slide 74
Wind Energy
Measuring wind speeds is crucial for planning the development of wind farms
Average wind speeds over a 10-15 minute deadline taken over several years are typically used
Heights of 10, 25 and 45m are used
  Typical heights of wind turbines
Typically wind speeds of around 10m/s are optimum
  As we shall see, the energy generated varies with the cube of the wind speed
Wind speeds greater that 25m/s cause a shut off of the turbine

## Slide 75
Wind Energy
The UK is one of the best locations for wind power in the world, and is considered to be the best in Europe
  Wind power produced about 9% of our electricity in 2013
In fact we are ranked as the world's sixth largest producer of wind power, having overtaken France and Italy in 2012
A growing proportion of our wind energy is off shore

## Slide 76
Biomass
Biomass is a renewable energy source that is derived from living or recently living organisms
Biomass includes biological material, not organic material like coal.
Energy derived from biomass is mostly used to generate electricity or to produce heat
Biomass can be sourced locally, from within the UK, on an indefinite basis, contributing to security of supply and has a much lower carbon footprint than fossil fuels
The waste matter will rot anyway if we don’t use it producing methane which is a potent greenhouse gas
  Drax power station now burns a large range of biomass, mostly imported from the USA and Canada

## Slide 77
A Comparison of Renewables
There are a number of ways to compare renewables such as cost/kWh, human disruption and so on
Renewables are diverse energy sources
  They take up space, unlike a fossil or nuclear fueled power station which can produce 1GW in less than 1km2
  We can compare the power per unit area of various renewables
  We can work out how much area it would take to run UK electricity (about 40GW)
  For example it would take 40 x 109 /3 m2 of offshore wind
    About an area of 100km x 100km which is half the size of Wales!
POWER PER UNIT LAND OR WATER AREA | 
Wind | 2 W/m2
Offshore wind | 3 W/m2
Tidal pools | 3 W/m2
Tidal stream | 6 W/m2
Solar PV panels | 5–20 W/m2
Plants | 0.5 W/m2
Rain-water (highlands) | 0.24 W/m2
Hydroelectric facility | 11 W/m2
Solar chimney | 0.1 W/m2
Concentrating solar | 15 W/m2

## Slide 78
A Comparison of Renewables
However, concentrated solar power is a realistic possibility of supplying the UK (and the World’s) energy needs
In deserts solar power can deliver typically 15W/m2 of power
So, chose your local desert
All the worlds power consumption (15000GW) could be delivered by an 1000km x 1000km of the Sahara desert
  Or taking the Sahara as the local desert for Europe, 600km x 600km (yellow square)
  Or the UK’s would be 145km x 145km (red square)
Easily transported using HVDC cables
Check out the DESERTEC video
  https://www.youtube.com/watch?feature=player_embedded&v=QXx02iMsDqI

## Slide 79
Summary
We have looked in detail at the sun’s incident radiation and Earth’s energy budget
Also we have looked at both non-renewable and renewable energy sources briefly
  In the next lecture we will look in a bit more detail about the generating power from these sources
    Including how much power is produced