## Slide 1: Computer Networking Queueing (A Summary from Appendix A)
Dr Sandra I. Woolley

## Slide 2: Queueing
Source : A summary of Appendix A
Delay analysis and Little’s formula
Basic queueing models

## Slide 3: Delay Analysis
A basic model for a delay/loss system
Time spent in system = T
No. customers in system = N(t)
Fraction of arriving customers that are lost or blocked = Pb
Long term arrival rate = 
Average no of messages/second that pass through = throughput
Delay box:
Multiplexer,
switch, or
network
Message,
packet,
cell
arrivals
Message,
packet,
cell
departures
T seconds
Lost or
blocked

## Slide 4: Key System Variables
From time 0 to time t:
  Number of arrivals at the system: A(t)
  Number of blocked customers: B(t)
  Number of departed customers: D(t)
Number of customers in system at time t (assuming system was empty at t = 0):
Long term arrival rate is:
Throughput is:
Average system occupancy is E[N]

## Slide 5: Arrival Rates and Traffic Loads
A(t)
t
0
1
2
n-1
n
n+1
Time of nth arrival = 1 + 2 + . . . + n
Arrival
Rate
n arrivals
1 + 2 + . . . + n seconds
=
1
=
1
(1+2 +...+n)/n
E[]
1
2
3
n
n+1
•••
Arrival Rate = 1 / mean interarrival time

## Slide 6: Little’s Formula
We need to link the average time spent in the system to the average number of customers in the system
Assume non-blocking system:
A(t)
D(t)
Delay Box
N(t)
T

## Slide 7: Little’s Formula
Little’s formula links the average time spent in the system to the average number of customers in the system
E[N] = ·E[T] (without blocking)
E[N] = ·(1 – Pb)E[T] (with blocking)
A(t)
D(t)
Delay Box
N(t)
T

## Slide 8: Application of Little’s formula
Consider an entire network of queueing systems
Little’s formula states that: E[Nnet] = netE[Tnet]
Thus, E[Tnet] = E[Nnet]/net
For the mth switch/multiplexer: E[Nm] = mE[Tm]
The total no of packets in the network is the sum of the total no of packets in the switches: E[Nnet] = Sm E[Nm] = Sm m·E[Tm]
Combining the above equations yields,
E[Tnet] = 1/net Sm m·E[Tm]
Network delay depends on overall arrival rate in network (offered traffic), arrival rate to individual routers (determined by routing algorithm) and delay in each router (determined by arrival rate, switching capacity and transmission line capacity)

## Slide 9: Basic Queueing Models
1
2
c
A(t)
t
D(t)
t
B(t)
Queue
Servers
Arrival process
X
Service time
i
i+1


## Slide 10: Queueing Model Classification
Service times X
M = exponential
D = deterministic
G = general
Service Rate:
E[X]
Arrival Process / Service Time / Servers / Max Occupancy
Interarrival times 
M = exponential
D = deterministic
G = general
Arrival Rate:
E[ ]
1 server
c servers
infinite
K customers
unspecified if
unlimited
Multiplexer Models: M/M/1/K, M/M/1, M/G/1, M/D/1
Trunking Models: M/M/c/c, M/G/c/c
User Activity: M/M/, M/G/ 

## Slide 11: Queueing System Variables
Useful for calculations:
E[N] = ·(1 – Pb)E[T]
E[Nq] = ·(1 – Pb)E[W]
E[Ns] = ·(1 – Pb)E[X]
Offered (traffic) load = / m Erlangs
(rate at which “work” arrives at system)
Carried load = / m (1 – Pb)
(average rate at which system does “work”)
1
2
c
X
Nq(t)
Ns(t)
N(t) = Nq(t) + Ns(t)
T = W + X
W
Pb

Pb)
N(t) = number in system
* Nq(t) = number in queue
* Ns(t) = number in service
T = total delay
W = waiting time
X = service time


## Slide 12: Thank You